## Slide 1
REDUNDANT MULTI-FLOOR
ENTERPRISE CAMPUS NETWORK
Design, Implementation, Security & Verification using Cisco Packet Tracer
Team Lead
Dhruv Gaidhane
Team Members
Vaibhav Mule, Tejas Bargal
Organization
NextGen Education
Assigned By
Harish Sir
Project Type
Group Project — 3 Members
01 / 15

## Slide 2
GROUP PROJECT • NEXTGEN EDUCATION
Problem Statement & Objectives
The Challenge
Traditional campus networks can suffer from single points of failure.
Different departments require network segmentation.
Network communication must remain available during link/device failures.
Device management must be secure.
IP addressing should be centrally managed.
Network traffic must be controlled using security policies.
Project Objectives
1
Implement VLAN-based segmentation
2
Provide inter-VLAN communication
3
Provide gateway redundancy using HSRP
4
Implement dynamic routing using OSPF
5
Implement link aggregation (EtherChannel/LACP)
6
Implement STP/PVST+ for loop prevention
7
Configure DHCP for automatic addressing
8
Configure SSH for secure management
9
Implement ACLs for traffic filtering
10
Verify connectivity and redundancy
02 / 15

## Slide 3
PHYSICAL & LOGICAL DESIGN — CISCO PACKET TRACER
Network Topology
R-CAMP1 / R-CAMP2 = core routers • DSW1 / DSW2 = 3560-24PS distribution (HSRP + EtherChannel) • Floor 1–3 access switches uplink redundantly to both
03 / 15

## Slide 4
METHODOLOGY
Project Flowchart
1
Requirement Analysis
2
Network Topology Design
3
Router & Switch Configuration
4
VLAN & IP Addressing
5
HSRP + OSPF + EtherChannel
6
DHCP & SSH Security
7
ACL Implementation
8
Connectivity & Network Testing
9
Troubleshooting & Verification
10
Final Secure & Redundant Network
04 / 15

## Slide 5
LAYER 2 / LAYER 3 DESIGN
VLAN & IP Addressing
VLAN | Department | Network | Gateway
10 | ADMIN | 10.10.10.0/24 | 10.10.10.1
20 | HR | 10.10.20.0/24 | 10.10.20.1
30 | FINANCE | 10.10.30.0/24 | 10.10.30.1
40 | DEVELOPMENT | 10.10.40.0/24 | 10.10.40.1
50 | TRAINING | 10.10.50.0/24 | 10.10.50.1
60 | SERVER | 10.10.60.0/24 | 10.10.60.1
99 | MANAGEMENT | 10.10.99.0/24 | 10.10.99.1
Design Notes
VLAN segmentation isolates department traffic
Separate broadcast domains per VLAN
Department-level traffic isolation
SVI-based gateways on the distribution switches
Structured, centrally-managed IP addressing
05 / 15

## Slide 6
LAYER 2 RESILIENCE
Distribution Layer & STP
DSW1
Primary Distribution Switch
✓
STP Root
✓
HSRP Active
✓
Layer-3 routing
✓
VLAN gateways
DSW2
Secondary Distribution Switch
✓
STP Secondary Root
✓
HSRP Standby
✓
Layer-3 routing
✓
VLAN gateways
STP / PVST+
Prevents Layer-2 loops
Predictable forwarding paths
Maintains backup paths
DSW1 = primary root
Simplified STP Path Illustration
DSW1
Root Bridge
DSW2
Alt. Bridge
ASW1
ASW2
ASW3
Dashed link = blocked (backup) path
06 / 15

## Slide 7
LINK AGGREGATION
EtherChannel / LACP
Concept
LACP is used for link aggregation
Multiple physical links act as one logical link
Improves redundancy across the DSW1–DSW2 link
Provides higher aggregate bandwidth
Removes dependence on a single physical link
show etherchannel summary
Po1(SU)
Gi0/1(P)
Gi0/2(P)
Aggregated Link
DSW1
DSW2
Port-Channel 1
Gi0/1 & Gi0/2 bundled into one logical link
2
Physical Links
1
Logical Link
LACP
Protocol Used
07 / 15

## Slide 8
GATEWAY REDUNDANCY
HSRP & Inter-VLAN Routing
Inter-VLAN Routing
Layer-3 switches use SVIs
Each VLAN has a default gateway
VLANs communicate through the distribution layer
HSRP
Provides a virtual default gateway
DSW1 = Active
DSW2 = Standby
End devices keep using the same virtual gateway during failure
Virtual GW
10.10.X.1
DSW1
Active (.2)
DSW2
Standby (.3)
HSRP hello / state sync
show standby brief
Interface Grp Pri State Active Standby
Vlan10 1 110 Active local 10.10.10.3
08 / 15

## Slide 9
LAYER 3 REDUNDANCY
OSPF Dynamic Routing
Implementation Details
OSPF Process ID: 1
Single-area design — Area 0
Router ID configured on each device
Dynamic route exchange between routers and switches
Redundant Layer-3 paths
Automatic route convergence on failure
show ip ospf neighbor / show ip route
Neighbor ID State Dead Time Interface
10.10.99.2 FULL/BDR 00:00:38 Gi0/0
Redundant Routed Paths (Area 0)
R-CAMP1
R-CAMP2
DSW1
DSW2
09 / 15

## Slide 10
AUTOMATIC ADDRESSING
DHCP Implementation
DHCP Request Flow
PC
▼
Access Switch
▼
DSW SVI
▼
DHCP Relay
▼
R-CAMP1
▼
DHCP Pool
▼
IP Address Assigned
Configuration Highlights
Separate DHCP pools defined for each VLAN
Automatic IP address assignment to end devices
Default gateway distributed via DHCP options
DNS server configuration included in each pool
DHCP relay using ip helper-address on router SVIs
DHCP bindings verified successfully
show ip dhcp binding
IP address Client-ID/Hw addr Lease expiration
10.10.10.10 0100.5079.6684.1a Automatic
10 / 15

## Slide 11
HARDENING THE CAMPUS
Network Security
1
SSH
Secure remote management
SSH version 2
Local authentication
2
ACL
Controls permitted/denied traffic
Restricts unauthorized communication
Applies traffic filtering policies
3
Port Security
Limits MAC addresses per port
Sticky MAC learning
Protects access ports
4
PortFast + BPDU Guard
Faster endpoint connectivity
Protects ports from unexpected BPDUs
✓
The ACL implementation has been completed and verified.
11 / 15

## Slide 12
VALIDATION
Connectivity & Network Testing
Test | Purpose | Result
Ping | End-to-end connectivity | ✓ PASS
Traceroute | Path verification | ✓ PASS
VLAN verification | VLAN configuration | ✓ PASS
Trunk verification | VLAN transport | ✓ PASS
EtherChannel | Link aggregation | ✓ PASS
HSRP | Gateway redundancy | ✓ PASS
OSPF | Routing adjacency | ✓ PASS
DHCP | IP assignment | ✓ PASS
SSH | Secure management | ✓ PASS
ACL | Traffic filtering | ✓ PASS
12 / 15

## Slide 13
REAL IMPLEMENTATION EVIDENCE
Troubleshooting & Challenges
Issue 1 — Trunk Configuration
PROBLEM
Trunk command rejected
CAUSE
Encapsulation was Auto
SOLUTION
Configure 802.1Q encapsulation before trunk mode
Issue 2 — R-CAMP2 Connectivity
PROBLEM
Routed link was not functioning
CAUSE
Incorrect/missing /30 addressing
SOLUTION
Correct the interface IP configuration
Issue 3 — Duplicate Transit IP
PROBLEM
Duplicate IP addressing on a transit interface
CAUSE
Misconfigured DSW1 transit address
SOLUTION
Correct the DSW1 transit address
Issue 4 — OSPF Neighbor
PROBLEM
OSPF adjacency was not established
CAUSE
Interface / addressing mismatch
SOLUTION
Verify interface status, IP addressing and OSPF configuration
Problem → Cause → Solution → Verification
13 / 15

## Slide 14
FINAL RESULTS
Verification & Final Results
Verified Components
✓
VLANs
✓
Trunks
✓
STP / PVST+
✓
EtherChannel / LACP
✓
HSRP
✓
Inter-VLAN Routing
✓
OSPF
✓
DHCP
✓
SSH
✓
ACL
✓
Port Security
✓
PortFast
✓
BPDU Guard
✓
End-to-End Connectivity
Outcome
The implemented network provides segmentation, redundancy, dynamic routing, secure management and traffic control.
Insert important Packet Tracer command-output screenshots here
14 / 15

## Slide 15
CONCLUSION & FUTURE SCOPE
A Secure + Redundant + Segmented + Dynamically Routed Enterprise Campus Network
Implemented and verified using Cisco Packet Tracer.
Key Achievements
✓
Department-based VLAN segmentation
✓
Redundant gateway using HSRP
✓
Dynamic routing using OSPF
✓
Link aggregation (EtherChannel/LACP)
✓
Layer-2 loop prevention via STP
✓
Centralized DHCP
✓
Secure SSH management
✓
ACL-based traffic control
✓
Access-layer port security
✓
End-to-end connectivity verified
Future Scope
Network monitoring using SNMP
Syslog-based centralized logging
Network automation
IPv6 implementation
Wireless integration
Advanced ACL policies
Firewall / IDS integration
Real-device deployment
15 / 15

## Slide 16
15 / 15
  Thank You